## Slide 1: VENUS THERMOSPHERIC DENSITIES AS REVEALED BY VENUS EXPRESS TORQUE MEASUREMENTS C.F. Wilson, Oxford University, Oxford, UK (wilson@atm.ox.ac.uk), M. Persson, Swedish Institute of Space Physics, Kiruna, Sweden. E. Grotheer, ESAC, Spain, I. Müller-Wodarg, Imperial College London, UK, S. Damiani, M. Müller, ESA/ESOC, Germany, H. Svedhem, ESA/ESTEC, Noordwijk, the Netherlands, P. Rosenblatt, Royal Observatory of Belgium, S. Bruinsma, CNES/GRGS, Toulouse.
Venus 2016 conference, Oxford

## Slide 2: Accelerometers: measure densities up to 150 km altitude Gyros / reaction wheels: measure densities up to 200 km altitude
Torque data
TorqueAD
vector
Compensate via reaction wheels
Wind
~8-10 km/s

## Slide 3: VEx Torque data reduction
Much of the introductory work was done by ESOC Flight dynamics team: Michael Müller, Sylvain Damiani, and others.
  Described in papers such as Damiani et al., 2013; Lorenzo et al., 2012.
However, the densities derived from their analyses were not made available for scientific analyses and are no longer available
Emmanuel Grotheer (ESTEC, now ESAC) recreated the data pipeline (2014).
Moa Persson (MSc student at Oxford) refined this pipeline (2015).

## Slide 4: Torque data reduction in order to get the aerodynamic torque
Gravity gradient torque
Solar radiation torque
X-axis
Y-axis
Z-axis

## Slide 5: Torque data reduction
ESOC calculated aerodynamic forces on dozens of faces (removing shaded faces)
Virtually all of the torque is due to the solar panels
Using only solar panel torques to calculated ρ leads to errors of up to 5% for VExADE geometries [Damiani et al 2013]
Therefore we have used only torque from aerodynamic pressure on solar panels to calculate densities

## Slide 6: Torque data reduction
Exclusion criteria:
  SNR < 15
  Calculated torque vector direction deviates from measured torque direction by > 20°
  “Sensitivity” < 2 x 107 m5s-2
  Limits data to typically < 200 km

## Slide 7: Validation against Precise Orbit Determination (tracking) results
Our densities are correlated with those obtained from tracking data
They are on average 20% lower than those from tracking.
Discrepancy with values from ESOC may be due to different geometry parameters used (spacecraft position & velocities, CoM & CoP vectors, SA rotation angles)
  Solar Array rotation angles stored in SPICE are different (by up to 0.5°) from those reported in “VEx Aerodrag Measurements” report (VEX-ESC-RP-5520_i1r0). Why?

## Slide 8: Uncertainties
Systematic errors | Change in parameter | Effect on density | Source
Accommodation coefficient, α | ± 0.02 | ± 10 % | Damiani et al. (2012)
Wind velocity | ± 1 % | ± 2 % | Calculations
Wind direction | Up to ± 5 deg from pericentre value | Up to ± 4 % | Damiani et al. (2012)
Altitude | ± 1 % | ± 0.1 % | Calculations
Solar array angles | ± 0.5 deg | ± 3 % | Calculations
Only using solar arrays in calculations |  | Up to ± 5 % | Damiani et al. (2012)
Centre of mass | 1 % | Negligible | Calculations
 Total systematic uncertainty: up to 25%

## Slide 9: Densities from Torque & aerobraking 100 pericentre passes, all at 75° - 90°N
Note: only data with 88° < SZA < 92° are plotted

## Slide 10: Densities from Torque & aerobraking
Note: all data plotted, with SZA correction
CO2 is most abundant species
Monatomic O is most abundant species

## Slide 11: Densities & scale heights from Torque

## Slide 12: SZA dependence from Torque
160 – 170 km
170 – 180 km
180 – 190 km
190 – 200 km

## Slide 13: SZA dependence from Torque & AB
The sensitivity of ρ to SZA does not increase with z in the 160-200 km range
The sensitivity to SZA is much greater than predicted by Hedin model

## Slide 14: Binned densities for ISSI intercomparison typically ~ 40% less than VIRA densities

## Slide 15: Variability
1. Day-to-day variability
2. Gravity Waves

## Slide 16
Variability - Gravity waves
Aerobraking - July 2014
Density oscillations – gravity waves?
Horizontal wl ~ 100 – 200 km
Δρ/ρ ~ 20 % (at 130 km)

## Slide 17
Density oscillations – gravity waves?
Horizontal wl ~ 100 – 200 km
Δρ/ρ ~ 20 % (at 130 km)

## Slide 18: Variability 2 - Gravity waves VEx Torque - Oct 2010
Density oscillations – gravity waves?
Horizontal wl ~ 100 – 200 km
Δρ/ρ ~ 30 % (at 170 km)
Day/night asymmetry:
Increasing with altitude

## Slide 19: Gravity Waves – VEx Torque
Density oscillations – gravity waves?
Horizontal wl ~ 100 – 300 km
Δρ/ρ ~ 30%

## Slide 20: Gravity Waves – VEx Torque
Observed / model
Observed / model
23 May 2011
Pericentre altitude: 167 km
27 May 2011
Pericentre altitude: 167 km

## Slide 21: Gravity Waves – VEx Torque
Observed / model
Observed / model
12 Jan 2011
Pericentre altitude: 176 km
03 May 2012
Pericentre altitude: 166 km

## Slide 22: What causes the density oscillations?

## Slide 23: What causes the density oscillations?
Gravity waves at 130 km were seen in non-LTE CO2 emission by VEx/VIRTIS
Horizontal wavelengths ~100-200 km
Waves appear to be triggered by polar vortex
But these are very small radiance variations, on order of 1% - much smaller than density variations observed in VExADE

## Slide 24: Gravity waves on Mars
Gravity waves from MRO aerobraking
(Fritts et al 2006)
Typical wavelengths of 100 km
Typical Δρ/ρ ~ 20%

## Slide 25: Titan thermospheric density variations
Cui et al. JGR 2013
Wavelength = 110 s
At 6 km/s this corresponds to 660 km
Scaling laws … ?

## Slide 26: Next steps
Write up results
  Mean ρ(z, SZA) from Torque & aerobraking
  First-order characterization of waves and day-to-day variability.
Get torque densities ready for ingestion to PSA.
Variability
  gravity waves: investigate possible relationship with VIRTIS non-LTE observations
  Day-to-day variability: compare variability Δρ/ρ as a function of p on different planets.
Implement this technique on future missions!